## Slide 1: Plan for Today
Finishing getting total energy deposited in an event.
Looking the real experimental data from NaI, and determination of detector resolution.
Smearing the data with measured detector resolution.
Storing this data in ROOT file
(Histogram and Ttree)
Finally making a comparison between experimental and simulated data.

## Slide 2: Where we left yesterday
Idea :
Instead of passing object of event action, use ManagerClasses to get the access to your EventAction
G4UserEventAction *evAction = const_cast<G4UserEventAction *>(G4RunManager::GetRunManager()→GetUserEventAction());
NaI_EventAction *myEvAction = static_cast<NaI_EventAction *>(evAction);

## Slide 3: Using G4AnalysisManager to Create ROOT TTree and Histograms in Geant4
Data Analysis with Geant4

## Slide 4: Introduction
- Geant4 provides built-in analysis tools for data handling
- G4AnalysisManager allows users to store simulation results in ROOT format
- Can be used to create histograms and TTrees

## Slide 5: Enabling G4AnalysisManager
Include the necessary header files:
#include "G4AnalysisManager.hh"
G4AnalysisManager *analyMan = G4AnalysisManager::Instance();

## Slide 6: Creating a ROOT File
Set the output file name:
analyMan->OpenFile("output.root");
Close the file at the end of the run:
analyMan->Write();
analyMan->CloseFile();

## Slide 7: Creating a Histogram
Define a histogram:
analyMan->CreateH1("Edep", "Energy Deposition", 100, 0., 10.);
Fill the histogram in SteppingAction:
analyMan->FillH1(1, energyDeposition);

## Slide 8: Creating a ROOT TTree
Create an Ntuple:
analyMan->CreateNtuple("EventTree", "Event Data");
analyMan->CreateNtupleDColumn("Energy");
analyMan->FinishNtuple();
Fill the tree with data in EventAction:
analyMan->FillNtupleDColumn(0, totalEnergy);
analyMan->AddNtupleRow();

## Slide 9: Running the Simulation
- Compile and run the Geant4 simulation
- ROOT file is generated after execution
- Use ROOT to analyze histograms and trees

## Slide 10: Viewing Results in ROOT
Open the ROOT file:
root -l output.root
Tbrowser b
Plot histogram:
TH1F* h = (TH1F*) _file0->Get("Edep");
h->Draw();
View the tree:
TTree* t = (TTree*) _file0->Get("EventTree");
t→Scan();
t→Print();
t->Show(10);